## Slide 1: Quantum-secure Covert Communication on Bosonic Channels
Raytheon BBN Technologies
Boulat A. Bash (boulat.bash@raytheon.com) with Andrei H. Gheorghe (Harvard), Monika Patel (Carl Zeiss), Jonathan L. Habif, Dennis Goeckel (UMass), Don Towsley (UMass), and Saikat Guha
November 2, 2016
“This document does not contain technology or technical data controlled under either the U.S. International Traffic in Arms Regulations or the U.S. Export Administration Regulations.”
Nature Communications 6, 8620 (2015)
Notes: CONTENT OWNERS: ALWAYS REVIEW CONTENT WITH YOUR EX/IM or CONTRACTS REPRESENTATIVE FOR APPROPRIATE MARKINGS
WARNING – Users should ensure they follow the layout instructions found in Raytheon Policy 5024-RG (Global Trade Compliance: Marking and Protection of U.S. Export-Controlled Technical Information) – with the full marking on the first page and a smaller carryover marking on subsequent pages, if required.
TITLE SLIDE PAGES
Security markings can be inserted by clicking into the text block of “Type EX/IM marking, if appropriate, as required by 5024-RG (ex. "ITAR Controlled")”.
INSIDE SLIDE PAGES
Security markings can be inserted by going into the Slide Master Template.
Go to the top menu bar, pull down “View”.
Click the “Slide Master” icon in the horizontal bar.
Click on the top Slide 1.
Type appropriate classification in header and footer.
This will then be applied to all slide pages (except the cover slide).

## Slide 2: Introduction
Much of modern security research is dedicated to preventing unauthorized message decoding
  Cryptography: exploit adversary’s computational limitations
  Information-theoretic secrecy: exploit adversary’s physical limitations
But what if that is not enough?
  Social unrest: government may shut down any, especially encrypted, transmissions
  Military: hide presence of any activity
  Privacy intrusion: it’s often the “meta-data” that is important
Covert communication conceals presence of messages in the first place
What are the fundamental limits of covert communication?
  Need quantum information theory to study physical limits

## Slide 3: Prior art: Steganography
Why not use digital steganography?
  Embedding overwrites covertext noise, which we can’t necessarily access in noisy communication channel scenario
  Requires transmission of stegotext, inapplicable when transmissions are prohibited
Source: User Cyp, Wikipedia
message
covertext
stegotext
Notes: Extract 2 LSBs from the trees, re-normalize.

## Slide 4: Spread spectrum communication
What is “safe” power level and how much can be transmitted without detection?
  Square root law for AWGN channels [Bash12, Bash13a]: must use average per-symbol power over channel uses; transmit no more than bits total
Optical detection systems are quantum-noise limited: must use quantum mechanics to derive limits under the most powerful adversary permissible by physics
Original signal
Noise floor
Transmitted signal
Power
Frequency
Notes: Drive POWER SPECTRAL DENSITY down

## Slide 5: Outline
Introduction
Preliminaries
Analysis of covert optical communication
Experimental results
Conclusion: Vision for Shadow Network Architecture

## Slide 6: Covert Communication Model
Alice has a noisy channel to Bob
Alice and Bob prepare by sharing a secret
Willie monitors his noisy channel from Alice for transmissions
Clipart source:
Artist Gerald_G, openclipart.org
Noise at adversary
is critical for covert communication
Noisy channel
Noisy channel

## Slide 7: Hypothesis testing
Willie attempts to classify observations of Alice’s channel as either noise or signal corrupted by noise
  Binary hypothesis test
Willie’s probability of error
Alice desires
Willie decides he saw
Noise
Signal+Noise
quiet
transmitting
Alice is
“Covertness” criterion

## Slide 8: Outline
Introduction
Preliminaries
Analysis of covert optical communication
Experimental results
Conclusion: Vision for Shadow Network Architecture

## Slide 9: Noiseless measurements on pure-loss channel
Bosonic channel is the quantum-mechanical description of an optical channel with linear loss (beamsplitter)
No covert communication possible!
Conditions unlikely to ever occur practically
  Noisy environment (Planck’s Law), non-ideal detectors
Vacuum environment
Semi-ideal single photon detector (SPD):
no false alarms
can miss transmissions
Any receiver
Any pre-shared secret
Arbitrary input over optical modes
Modes are orthogonal signals, #modes is time-bandwidth product

## Slide 10: Thermal noise channel
Beamsplitter models the optical channel
Square root law: Alice can reliably transmit covert bits using optical modes, and no more
  Mean photon number (power) per mode photons to hide in the noise
Thermal environment
Quantum-optimal receiver
Homodyne receiver or noisy single photon detector:
Laser
input:
Pre-shared secret
Pre-shared secret
Modes are orthogonal signals, #modes is time-bandwidth product
Notes: Environment is in a thermal state, mixture of coherent states weighted by complex Gaussian distribution.
Alice uses zero-mean isotropic Gaussian-distributed coherent state codewords.

## Slide 11: Outline
Introduction
Preliminaries
Analysis of covert optical communication
Experimental results
Conclusion: Vision for Shadow Network Architecture

## Slide 12: Experimental setup
Alice 1 ns pulses
1.5 m wavelength
Variable attenuator
Willie (SPD)
Bob (SPD)
Mirror
PBSC
Message generation,
encoding
NI PCIe-6537 DAQ board
Detection
Message
decoding
Linear
polarizer
HWP
Laser driver
1 MHz clock

## Slide 13: Experimental setup
NI DAQ Board
Willie’s
SPD
Output (laser)
Trigger
Bob’s
SPD
Input (detector)
trigger
External clock
Alice
Bob
Willie
Pulsed laser
Pulse
generator
Temperature
control
Variable
attenuator

## Slide 14: Experimental setup

## Slide 15: Number of bits received by Bob
Bits decoded by Bob
102
103
104
3.2105
3.2106
3.2107
Optical modes ()
Careful Alice,
Careless Alice,
Dangerously
careless Alice
Points: average of 100 experiments using
(31,15) R-S code over order PPM;
95% CI negligible
Lines: maximum throughput (Shannon)

## Slide 16: Willie detection error probability
Careful Alice,
Careless Alice,
Dangerously
careless Alice
Detection Error Probability
3.2105
3.2106
3.2107
0.1
0.2
0.3
0.4
0.5
Willie’s optimal detector: LRT LRT statistic: total click count
Line: Gaussian approximation
Solid fill: 100 experiments, 95% CI ±0.136
Clear fill: 10k MonteCarlo sims, 95% CI ±0.014
Optical modes ( )

## Slide 17: What is the optimal center bandwidth?
Lesser diffraction loss, more spatial modes; Less background noise
Greater diffraction loss, less spatial modes; More background noise
time
space
polarization
#modes

## Slide 18: Conclusion: Vision for Shadow Network Architecture
JR
JR
Covert use of existing wired networks [Soltani15, Soltani16]
Covert sensing
Covert optical network
Covert RF network
Dynamic switching between jamming and relaying
Piggybacking covert info on existing transmissions
Jamming enables covert bits in channel uses [Sobers15, Sobers16]
Ongoing projects:
  DARPA Defense Sciences Office QUIET program (BBN and UMass)
  NSF Limits and Algorithms for Covert Communications (UMass)
asynchrony issues [Bash14, Goeckel15, Bash16]
space

## Slide 19: Backup slides

## Slide 20: Proof construction for practical receivers
On-off keying modulation, random code, ML decode
  Probability of “on” pulse ensures stealth with secret codebook
Easy analysis but implementation impractical
  Desire to use structured, public error correction code (ECC)
0 | 0 | 0 | … | 0 | 0
0 | 0 | 0 | … | 0 | 1
1 | 1 | 1 | … | 1 | 1
…
Messages
Random codewords
optical modes
bits

## Slide 21: Pulse-position modulation (PPM) signaling
Pulse-position modulation (PPM) signaling uses pulse location to encode value:
Then use an outer ECC on top of PPM
Challenge for covert communication: every PPM symbol requires a pulse, zero pulses not allowed
Value:
optical modes
PPM frame
1
2
Q

## Slide 22: Using PPM Alphabet
Solution: given possible PPM frames, Alice and Bob secretly agree on a random subset to use for message transmission,
Bob ignores the “empty” frames, but Willie cannot since he doesn’t know where they are
Alice transmits:
Bob receives:
Willie receives:
- transmitted pulses
- dark clicks
- PPM frame
optical modes
PPM frames, optical modes

## Slide 23: Covert communication with PPM
Alice and Bob also construct vector secretly, with each chosen uniformly at random from
Alice transmits using frames in
Bob subtracts modulo , then decodes
Willie cannot exploit ECC structure
SRL: Alice can reliably transmit covert bits in optical channel uses with public random code
However, we use Reed-Solomon for experiments
Codeword
Transmission

## Slide 24: Experimental design
Data
  100 testbed experiments per data point
  10k Monte-Carlo simulations per data point (Willie only)
    Simulate optical channel induced by laser-light transmitter and SPD using measured testbed characteristics
Bob
  PPM, (31,15) Reed-Solomon ECC
  Report average number of decoded bits
  Observed characteristics  max throughput from Shannon capacity
Willie
  Optimal detector = LRT
  Estimate from empirical distributions of LRT statistics
  LRT statistic ≈ total click count  Gaussian approximation

## Slide 25: References (1)
Spread spectrum technology references:
  [Simon94] Simon et al., “Spread Spectrum Communications Handbook,” McGraw Hill, New York, NY (1994).
  [Nicholson88] D.L. Nicholson, “Spread Spectrum Signal Design: LPE and AJ Systems,” Computer Science Press, Rockville, MD (1988)
Our work on covert communication:
  [Bash12] B. A. Bash†, D. Goeckel, and D. Towsley, “Square Root Law for Communication with Low Probability of Detection on AWGN Channels,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Cambridge, MA (2012)
  [Bash13a] B. A. Bash†, D. Goeckel, and D. Towsley, “Limits of reliable communication with low probability of detection on AWGN channels,” IEEE J. Sel. Areas Commun. 31 (9), 1921-1930 (2013).
  [Bash13b] B.A. Bash†, S. Guha†, D. Goeckel, and D. Towsley, “Quantum Noise Limited Optical Communication with Low Probability of Detection,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Istanbul, Turkey (2013)
  [Bash14] B. A. Bash†, D. Goeckel, and D. Towsley, “LPD Communication when the Warden Does Not Know When,” Proc. IEEE Int. Symp. Inf. Theory (ISIT),Honolulu, Hawaii (2014).
†Raytheon BBN QuIP Staff Member

## Slide 26: References (2)
Our work on covert communication (continued):
  [Soltani14] R. Soltani, B. A. Bash†, D. Goeckel, S. Guha†, and D. Towsley, “Artificial Noise Generation to Enhance LPD Throughput on AWGN Channels” Proc. Conf. on Commun., Control, Comp. (Allerton), Monticello, IL (2014)
  [Bash15a] B. A. Bash†, “Fundamental Limits of Covert Communication,” Ph.D. Thesis, University of Massachusetts, Amherst (2015)
  [Bash15b] B. A. Bash†, D. Goeckel, S. Guha†, and D. Towsley, “Hiding Information in Noise: Fundamental Limits of Covert Communication,” IEEE Commun. Mag. 53 (12), 26-31 (Dec 2015).
  [Bash15c] B. A. Bash†, A.H. Gheorghe, M. Patel, J. L. Habif†, D. Goeckel, D. Towsley, and S. Guha†, “Quantum-secure Covert Communication on Bosonic Channels,” Nature Communications 6, 8620 (2015).
  [Sobers15] T. Sobers, B. A. Bash†, D. Goeckel, S. Guha†, and D. Towsley, “Covert Communication with the Help of an Uninformed Jammer Achieves Positive Rate,” Proc. Asilomar Conf. on Signals, Syst. and Comput., Pacific Grove, CA (2015)
†Raytheon BBN QuIP Staff Member

## Slide 27: References (3)
Our work on covert communication (continued):
  [Goeckel16] D. Goeckel, B. A. Bash†, S. Guha†, and D. Towsley, “Covert Communications when the Warden Does Not Know the Background Noise Power,” IEEE Communications Letters (2016)
  [Sobers16] T. Sobers, B. A. Bash†, S. Guha†, D. Towsley, and D. Goeckel, “Covert Communication in the Presence of an Uninformed Jammer,” in submission (2016), arXiv:1608.00698v1 [cs.IT]
  [Sheikholeslami16] A. Sheikholeslami, B. A. Bash†, D. Goeckel, D. Towsley, and S. Guha†, “Covert communication over classical-quantum channels,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Barcelona, Spain (2016) arXiv:1601.06826 [quant-ph]
  [Soltani15] R. Soltani, D. Goeckel, D. Towsley, and A. Houmansadr, “Covert communications on poisson packet channels,” Proc. Conf. on Commun., Control, Comp. (Allerton), Monticello, IL (2015)
  [Soltani16] R. Soltani, D. Goeckel, D. Towsley, and A. Houmansadr, “Covert communications on renewal packet channels,” arXiv:1610.00368 [cs.IT] (2016)
†Raytheon BBN QuIP Staff Member

## Slide 28: References (4)
Sample of the follow-on work by other groups:
  [Che13] P.H. Che, M. Bakshi, S. Jaggi “Reliable deniable communication: Hiding messages in noise,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Istanbul, Turkey (2013)
  [Kadhe14] S. Kadhe, S. Jaggi, M. Bakshi, A. Sprintson, “Reliable, Deniable, and Hidable Communication over Multipath Networks,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Honolulu, Hawaii (2014).
  [Hou14] J. Hou and G. Kramer, “Effective secrecy: Reliability, confusion and stealth,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Honolulu, Hawaii (2014)
  [Che14] P.H. Che, M. Bakshi, C. Chan, S. Jaggi “Reliable Deniable Communication with Channel Uncertainty” Proc. IEEE Inf. Theory Workshop (ITW), Hobart, Australia (2014)
  [Lee14] S. Lee, and R. J. Baxley, “Achieving positive rate with undetectable communication over AWGN and Rayleigh channels,” Proc. IEEE Int. Conf. Commun. (ICC) pp. 780-785, (2014).
  [Lee15] S. Lee, R. J. Baxley, M.A. Weitnauer, and B. Walkenhorst, “Achieving Undetectable Communication,” IEEE J. Sel. Topics Signal Process., forthcoming.

## Slide 29: References (5)
Sample of the follow-on work by other groups (continued):
  [Wang15] L. Wang, L. Zheng, G. W. Wornell, “Limits of Low-Probability-of-Detection Communication over a Discrete Memoryless Channel,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Hong Kong, China (2015).
  [Bloch15] M. Bloch, “Covert Communication over Noisy Channels: A Resolvability Perspective,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Hong Kong, China (2015), arXiv:1503.08778 [cs.IT] (2015)
  [Tahmasbi16] M. Tahmasbi and M. Bloch, “Second-Order Asymptotics of Covert Communications over Noisy Channels,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Barcelona, Spain (2016)
  [Arumugam16a] K.S.K. Arumugam and M. Bloch “Keyless Covert Communication over Multiple-Access Channels,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Barcelona, Spain (2016)
  [Zhang16] Q. Zhang, M. Bakshi, and S. Jaggi, “Computationally Efficient Deniable Communication,” Proc. IEEE Int. Symp. Inf. Theory (ISIT), Barcelona, Spain (2016)
  [Arumugam16b] K.S.K. Arumugam and M. Bloch “Keyless asynchronous covert communication,” Proc. Inform. Theory Workshop (ITW), Cambridge, UK (2016)